## Slide 1
WEEK 6 – Auxiliary Projection – Self-learning

## Slide 2
WEEK 6 – Auxiliary Projection – Assignments
Finish – E12, E13, E14
Submit – E13

## Slide 3
WEEK 6 – Recap
1st Angle Projection: Projection behind the object
3rd Angle Projection: Projection in front of the object
Auxiliary Plan: Projected from the elevation view
Auxiliary Elevation: Projected from the plan view

## Slide 4
AUXILIARY PROJECTION - Recap
1. Reproduce the principal views (Elevation & Plan)
2. Projectors parallel to the given direction from end points
3. Ground line perpendicular to the projectors
4. Transfer heights/widths

## Slide 5
AUXILIARY PROJECTION – CURVES APPROXIMATION
How many points ? Up to you
Generally: 2 pts in the middle for a quarter of a circle
30°
30°
30°
L/3
L/3
L/3
L

## Slide 6
AUXILIARY PROJECTION – FURTHEST POINTS
Generally: draw a line to connect furthest points (visible – solid; invisible – dashed).

## Slide 7
AUXILIARY PROJECTION – EDGE OF COLUMNS
Generally: draw a line to connect furthest points (visible – solid; invisible – dashed).
90°
View direction
Inner surface

## Slide 8
AUXILIARY PROJECTION – HIDDEN LINES
When a hidden line coincide with a solid line, only keep the SOLID line.

## Slide 9
AUXILIARY PROJECTION – HIDDEN LINES
Visible lines/curves, use solid lines/curves;
Hidden lines/curves, use dashed lines/curves.
‘Layer Properties’ > ‘Linetype’ to change solid/dashed lines

## Slide 10
AUXILIARY PROJECTION – BREAK AT A POINT
‘Modify’ > ‘Break at a point’: break the line into 2 parts

## Slide 11
AUXILIARY PROJECTION – HIDDEN LINES & BREAK AT A POINT – EXAMPLE - Video

## Slide 12
WEEK 6 – Prepare for Quiz 1
Scope: Auxiliary Projection
Review: E9-E14

## Slide 13
WEEK 6 – Prepare for Quiz 1
SEATING – Every Other Column
QUIZ PAPER (cannot be taken out) – Write down Name + Matr.No.
NO INTERNET CONNECTION, ONLY NTULearn Access
Files to submit: DWG + PDF

## Slide 14
WEEK 6 – Prepare for Quiz 1
Export DWG:
‘FILE’ > ‘Save As’ > ’.dwg’
Export PDF:
‘Layout’ tab > Type ‘print’ > Select printer ‘Microsoft print to pdf’ > ‘Preview’ to check > ‘ESC’ exit preview > ‘OK’ to save PDF file

## Slide 18
Where to download the slides?